## Slide 1: Chapter 4: Ethernet
Introduction to Networks

## Slide 2: Chapter 5: Objectives
Upon completion of this chapter, you will be able to:
Describe the operation of the Ethernet sublayers.
Identify the major fields of the Ethernet frame.
Describe the purpose and characteristics of the Ethernet MAC address.
Describe the purpose of ARP.
Explain how ARP requests impact network and host performance.
Explain basic switching concepts.
Compare fixed configuration and modular switches.
Configure a Layer 3 switch.

## Slide 3: Chapter 4
4.0 Introduction
4.1 Ethernet Protocol
4.2 Address Resolution Protocol
4.3 LAN Switches
4.4 Summary
Notes: Chapter 5 Sections

## Slide 4: 4.1 Ethernet Protocol
Notes: 5.1 Ethernet Protocol

## Slide 5: Ethernet Operation LLC and MAC Sublayers
Ethernet
  One of the most widely used LAN technologies
  Operates in the data link layer and the physical layer
  Family of networking technologies that are defined in the IEEE 802.2 and 802.3 standards
  Supports data bandwidths of 10, 100, 1000, 10,000, 40,000, and 100,000 Mbps (100 Gbps)
Ethernet Standards
  Define Layer 2 protocols and Layer 1 technologies
  Two separate sub layers of the data link layer to operate – Logical link control (LLC) and the MAC sublayers

## Slide 6: Ethernet Operation LLC and MAC Sublayers (cont.)
Notes: 5.1.1.1 LLC and MAC Sublayers (cont.)

## Slide 7: Ethernet Operation LLC and MAC Sublayers (cont.)
LLC
Handles communication between upper and lower layers.
Takes the network protocol data and adds control information to help deliver the packet to the destination.
MAC
Constitutes the lower sublayer of the data link layer.
Implemented by hardware, typically in the computer NIC.
Two primary responsibilities:
    Data encapsulation
    Media access control
Notes: 5.1.1.1 LLC and MAC Sublayers (cont.)

## Slide 8: Ethernet Operation MAC Sublayer

## Slide 9: Ethernet Operation MAC Sublayer (cont.)
Data encapsulation
Frame assembly before transmission and frame disassembly upon reception of a frame.
MAC layer adds a header and trailer to the network layer PDU.
Provides three primary functions:
Frame delimiting – Identifies a group of bits that make up a frame, synchronization between the transmitting and receiving nodes.
Addressing – Each Ethernet header added in the frame contains the physical address (MAC address) that enables a frame to be delivered to a destination node.
Error detection – Each Ethernet frame contains a trailer with a cyclic redundancy check (CRC) of the frame contents.
Notes: 5.1.1.2 MAC Sublayer (cont.)

## Slide 10: Ethernet Operation MAC Sublayer (cont.)
MAC
Responsible for the placement of frames on the media and the removal of frames from the media
Communicates directly with the physical layer
If multiple devices on a single medium attempt to forward data simultaneously, the data will collide resulting in corrupted, unusable data
Ethernet provides a method for controlling how the nodes share access through the use a Carrier Sense Multiple Access (CSMA) technology
Notes: 5.1.1.2 MAC Sublayer (cont.)

## Slide 11: Ethernet Operation Media Access Control
Carrier Sense Multiple Access (CSMA) process
Used to first detect if the media is carrying a signal
If no carrier signal is detected, the device transmits its data
If two devices transmit at the same time - data collision
Notes: 5.1.1.3 Media Access Control

## Slide 12: Ethernet Operation Media Access Control (cont.)

## Slide 13: Ethernet Operation Media Access Control (cont.)
CSMA is usually implemented in conjunction with a method for resolving media contention. The two commonly used methods are: CSMA/Collision Detection and CSMA/Collision Avoidance
CSMA/Collision Detection
The device monitors the media for the presence of a data signal
If a data signal is absent, indicating that the media is free, the device transmits the data
If signals are then detected that show another device was transmitting at the same time, all devices stop sending & try again later
While Ethernet networks are designed with CSMA/CD technology, with today’s intermediate devices, collisions do not occur and the processes utilized by CSMA/CD are really unnecessary
Wireless connections in a LAN environment still have to take collisions into account
Notes: 5.1.1.3 Media Access Control (cont.)

## Slide 14: Ethernet Operation Media Access Control (cont.)
CSMA/Collision Avoidance (CSMA/CA) media access method
Device examines the media for the presence of data signal - if the media is free, the device sends a notification across the media of its intent to use it
The device then sends the data.
Used by 802.11 wireless networking technologies
Notes: 5.1.1.3 Media Access Control (cont.)

## Slide 15: Ethernet Operation MAC Address: Ethernet Identity
Layer 2 Ethernet MAC address is a 48-bit binary value expressed as 12 hexadecimal digits.
IEEE requires a vendor to follow these rules:
  Must use that vendor's assigned OUI as the first 3 bytes.
  All MAC addresses with the same OUI must be assigned a unique value in the last 3 bytes.

## Slide 16: Ethernet Operation Frame Processing
MAC addresses assigned to workstations, servers, printers, switches, and routers.
Example MACs:
  00-05-9A-3C-78-00
  00:05:9A:3C:78:00
  0005.9A3C.7800.
When a device is forwarding a message to an Ethernet network, attaches header information to the packet, contains the source and destination MAC address.
Each NIC views information to see if the destination MAC address in the frame matches the device’s physical MAC address stored in RAM.
No match, the device discards the frame.
Matches the destination MAC of the frame, the NIC passes the frame up the OSI layers, where the de-encapsulation process takes place.

## Slide 17: Ethernet Frame Attributes Ethernet Encapsulation
Early versions of Ethernet were slow at 10 Mb/s.
Now operate at 10 Gb/s per second and faster.
Ethernet frame structure adds headers and trailers around the Layer 3 PDU to encapsulate the message being sent.
Ethernet II is the Ethernet frame format used in TCP/IP networks.
Comparison of 802.3 and Ethernet II Frame Structures and Field Size

## Slide 18: Ethernet Frame Attributes Ethernet Frame Size
Ethernet II and IEEE 802.3 standards define the minimum frame size as 64 bytes and the maximum as 1518 bytes
Less than 64 bytes in length is considered a "collision fragment" or "runt frame”
If size of a transmitted frame is less than the minimum or greater than the maximum, the receiving device drops the frame
At the physical layer, different versions of Ethernet vary in their method for detecting and placing data on the media
Notes: 5.1.2.2 Ethernet Frame Size

## Slide 19: Ethernet Frame Attributes Ethernet Frame Size (cont.)
The figure displays the fields contained in the 802.1Q VLAN tag
Notes: 5.1.2.2 Ethernet Frame Size (cont.)

## Slide 20: Ethernet Frame Attributes Introduction to the Ethernet Frame
Preamble and Start Frame Delimiter Fields –
Used for synchronization between the sending and receiving devices.
Length/Type Field –
Defines the exact length of the frame's data field; describes which protocol is implemented.
Data and Pad Fields –
Contains the encapsulated data from a higher layer, an IPv4 packet.
Notes: 5.1.2.3 Introduction to the Ethernet Frame

## Slide 21: Ethernet Frame Attributes Introduction to the Ethernet Frame (cont.)
Frame Check Sequence Field
Used to detect errors in a frame with cyclic redundancy check (4 bytes); if calculations match at source and receiver, no error occurred.
Notes: 5.1.2.3 Introduction to the Ethernet Frame (cont.)

## Slide 22: Ethernet MAC MAC Addresses and Hexadecimal

## Slide 23: Ethernet MAC MAC Address Representations
Notes: 5.1.3.2 MAC Address Representations

## Slide 24: Ethernet MAC Unicast MAC Address

## Slide 25: Ethernet MAC Broadcast MAC Address

## Slide 26: Ethernet MAC Multicast MAC Address
Multicast MAC address is a special value that begins with 01-00-5E in hexadecimal
Range of IPV4 multicast addresses is 224.0.0.0 to 239.255.255.255

## Slide 27: MAC and IP MAC and IP
MAC Address
This address does not change
Similar to the name of a person
Known as physical address because physically assigned to the host NIC
IP Address
Similar to the address of a person
Based on where the host is actually located
Known as a logical address because assigned logically
Assigned to each host by a network administrator
Both the physical MAC and logical IP addresses are required for a computer to communicate just like both the name and address of a person are required to send a letter.

## Slide 28: Ethernet MAC End-to-End Connectivity, MAC, and IP
IP Packet Encapsulated in an Ethernet Frame
Notes: 5.1.4.2 End-to-End Connectivity, MAC, and IP

## Slide 29: Ethernet MAC End-to-End Connectivity, MAC, and IP (cont.)
Notes: 5.1.4.2 End-to-End Connectivity, MAC, and IP (cont.)

## Slide 30: 4.2 Address Resolution Protocol

## Slide 31: ARP Introduction to ARP
ARP Purpose
Sending node needs a way to find the MAC address of the destination for a given Ethernet link
The ARP protocol provides two basic functions:
Resolving IPv4 addresses to MAC addresses
Maintaining a table of mappings
Notes: 5.2.1.1 Introduction to ARP

## Slide 32: ARP Introduction to ARP (cont.)
Notes: 5.2.1.1 Introduction to ARP

## Slide 33: ARP ARP Functions/Operation
ARP Table
Used to find the data link layer address that is mapped to the destination IPv4 address.
As a node receives frames from the media, it records the source IP and MAC address as a mapping in the ARP table.
ARP Request
Layer 2 broadcast to all devices on the Ethernet LAN.
The node that matches the IP address in the broadcast will reply.
If no device responds to the ARP request, the packet is dropped because a frame cannot be created.
Note: Static map entries can be entered in an ARP table, but this is rarely done.

## Slide 34: ARP ARP Operation

## Slide 35: ARP ARP Operation (cont.)

## Slide 36: ARP ARP Operation (cont.)
Notes: 5.2.1.3 ARP Operation (cont.)

## Slide 37: ARP ARP Operation (cont.)
Notes: 5.2.1.3 ARP Operation (cont.)

## Slide 38: ARP ARP Functions/Operation (cont.)
Notes: 5.2.1.3 ARP Operation (cont.)

## Slide 39: ARP ARP Role in Remote Communication
If the destination IPv4 host is on the local network, the frame will use the MAC address of this device as the destination MAC address.
If the destination IPv4 host is not on the local network, the source uses the ARP process to determine a MAC address for the router interface serving as the gateway.
In the event that the gateway entry is not in the table, an ARP request is used to retrieve the MAC address associated with the IP address of the router interface.

## Slide 40: ARP Removing Entries from an ARP Table
The ARP cache timer removes ARP entries that have not been used for a specified period of time.
Commands may also be used to manually remove all or some of the entries in the ARP table.

## Slide 41: ARP ARP Tables on Networking Devices
Notes: 5.2.1.6 ARP Tables on Networking Devices

## Slide 42: ARP Issues How ARP Can Create Problems

## Slide 43: ARP Issues Mitigating ARP Problems

## Slide 44: 4.3 LAN Switches
Notes: Nhớ lại rằng các mô hình logic của một mạng Ethernet là một bus truy cập, trong đó các thiết bị tất cả các truy cập chia sẻ để cùng một môi trường. topo logic này xác định cách các host trên mạng xem và trình khung được gửi và nhận được trên mạng. Tuy nhiên, các mô hình vật lý của hầu hết các mạng Ethernet hiện nay là của một ngôi sao hoặc sao mở rộng. Điều này có nghĩa rằng trên hầu hết các mạng Ethernet, thiết bị đầu cuối thường được kết nối, trong một cơ sở point-to-point, để một Layer 2 LAN switch. Một lớp 2 LAN switch thực hiện chuyển đổi và lọc chỉ dựa trên các liên kết dữ liệu OSI lớp (Layer 2) địa chỉ MAC. Bộ chuyển mạch là hoàn toàn minh bạch để các giao thức mạng và các ứng dụng người dùng. Một switch Layer 2 xây dựng một bảng địa chỉ MAC mà nó sử dụng để đưa ra quyết định chuyển tiếp. Layer 2 công tắc phụ thuộc vào router để truyền dữ liệu giữa các mạng con IP độc lập.

## Slide 45: Switching Switch Port Fundamentals
Layer 2 LAN Switch
Connects end devices to a central intermediate device on most Ethernet networks
Performs switching and filtering based only on the MAC address
Builds a MAC address table that it uses to make forwarding decisions
Depends on routers to pass data between IP subnetworks

## Slide 46: Switching Switch MAC Address Table
1. The switch receives a broadcast frame from PC 1 on Port 1.
2. The switch enters the source MAC address and the switch port that received the frame into the address table.
3. Because the destination address is a broadcast, the switch floods the frame to all ports, except the port on which it received the frame.
4. The destination device replies to the broadcast with a unicast frame addressed to PC 1.

## Slide 47: Switching Switch MAC Address Table (cont.)
5. The switch enters the source MAC address of PC 2 and the port number of the switch port that received the frame into the address table. The destination address of the frame and its associated port is found in the MAC address table.
6. The switch can now forward frames between source and destination devices without flooding, because it has entries in the address table that identify the associated ports.
Notes: 5.3.1.2 Switch MAC Address Table (cont.)

## Slide 48: Switching Duplex Settings

## Slide 49: Switching Auto-MDIX

## Slide 50: Switching Frame Forwarding Methods on Cisco Switches

## Slide 51: Switching Cut-through Switching
Fast-forward switching:
Lowest level of latency immediately forwards a packet after reading the destination address, typical cut-through method of switching
Fragment-free switching:
Switch stores the first 64 bytes of the frame before forwarding, most network errors and collisions occur during the first 64 bytes

## Slide 52: Switching Memory Buffering on Switches

## Slide 53: Fixed or Modular Fixed versus Modular Configuration

## Slide 54: Chapter 4 Summary
Ethernet is the most widely used LAN technology used today.
Ethernet standards define both the Layer 2 protocols and the Layer 1 technologies.
The Ethernet frame structure adds headers and trailers around the Layer 3 PDU to encapsulate the message being sent.
As an implementation of the IEEE 802.2/3 standards, the Ethernet frame provides MAC addressing and error checking.
Replacing hubs with switches in the local network has reduced the probability of frame collisions in half-duplex links.
The Layer 2 addressing provided by Ethernet supports unicast, multicast, and broadcast communications.
Ethernet uses the Address Resolution Protocol to determine the MAC addresses of destinations and map them against known Network layer addresses.
Notes: Summary

## Slide 55: Chapter 4 Summary (cont.)
Each node on an IP network has both a MAC address and an IP address.
The ARP protocol resolves IPv4 addresses to MAC addresses and maintains a table of mappings.
A Layer 2 switch builds a MAC address table that it uses to make forwarding decisions.
Layer 3 switches are also capable of performing Layer 3 routing functions, reducing the need for dedicated routers on a LAN.
Layer 3 switches have specialized switching hardware so they can typically route data as quickly as they can switch.
Notes: Summary